## Slide 1: NSW Energy Savings Scheme (ESS) Training
Carbon Blue Requirements

## Slide 2: ESS Background
The Energy Savings Scheme started in 2009 and will extended to 2025.
The scheme is designed to encourage investment in energy efficiency through financial incentives.
Market based scheme that works by placing an obligation on the ‘Liable Entities’, mainly electricity retailers in NSW, to undertake or pay for energy efficiency programs.
Scheme is administered by the government and passed legislation that retailers must purchase the credit. The energy retailers must purchase ESC based off amount of MWh that they sell.
Retailers pass charge back onto energy bills.
Legislation has been put in place to ensure that the scheme does not gain a bad reputation and we as an ACP must ensure we meet all compliance requirements else we loose our license.

## Slide 3: Market Based http://greenmarkets.com.au/

## Slide 4
The cost of energy savings certificates is returned to the businesses who generate them
(Start) Businesses invest in better technology to reduce their energy use
Energy savings certificates are generated through the reduction in energy use
Liable parties such as electricity retailers buy energy savings certificates
If the ESC’s are processed as part of the project it’s a discount off the project whereas if post project it is treated as taxable income.
Only an ACP can create and trade ESC’s

## Slide 5: What creates an ESC 1 ESC (energy savings certificate = 1 tonne CO2-e saved (just less than 1 MWh) Old Load (W) – New Load (W) x hours x 10 years / 1000 = X MWh
Example:
Twin 36W T8 Recessed Troffer with B2 Ballast upgraded to 31W LED Panel located in air conditioned Office
2 x 36W (T8 Flouro Tube) = 72W
2 x 8W (B2 Ballast) = 16W
Total Old Load = 88W
Less New Load = 31W
Energy Savings = 57W x 1.3 Factor for Air Conditioning
= 74.1W x 3,000 Hours (office)
= 222,300 WH x 10 Years /1,000
= 2.22 MWH x 1.06 Emissions Factor
= 2.36 tCO2-e/ESC

## Slide 6: NSW ESS – Hours of Operation for Different BCA Classifications

## Slide 7: Examples
One 400W Mercury Vapour Highbay replaced with a 110W LED Highbay creates 14.5 ESC in a warehouse (5,000 hours)
One twin T8 with B2 ballast replaced with 31W LED panel creates 2.36 ESC in an air-conditioned office.
                Multipliers for:
                Control Systems 25% depending on which control
                Air Conditioning 30%

## Slide 8: CO2 Free - ACP
Carbon Blue uses CO2 Free as its licensed accredited certificate provider (ACP) to create the certificates
Administered by IPART whose costs are covered by $0.80 registration fee/ESC paid by ACP
Subject to regular audits to ensure compliance and no fraud – audit costs paid by ACP
Must collect and save evidence of the energy saving activity in order to create ESC.
Important that Carbon Blue is engaged at start of project to ensure all evidence is collected.
NSW government has given CO2 Free a license to operate as an ACP and to ensure we maintain that license we must operate according to regulatory requirements.

## Slide 9: Evidence Requirements
Original Energy Saver details (who pays electricity bill)
Existing End User Equipment (existing lighting)
Upgrade equipment (new lighting)
Installer details and forms
Financial records (tax invoices, payment receipts)
Recycling
Who collects what? - We will work with you and the contractor

## Slide 10: Original Energy Saver Evidence Required At Quotation Stage
OES Must be provided with ESS information as per legislation
Business name and ABN (required for compliance purposes)
Address (full) – must match electricity bill
Copy of electricity bill (Needed to work out accurate ROI)
Contact
  Name
  Position
  Email
  Phone
Type of premises, eg Office, Warehouse, Carpark (to determine allowable hours of operation)
Description of Areas and whether they contain air conditioning (30% extra) or lighting controls
Photo of front of the business(geotagged)

## Slide 11: Existing Lighting
For quotation Purposes:
Description of existing lights – eg twin 36W T8 in IP65
Ballast details, if unknown be conservative
Count in each space
Floor plan and dimensions + ceiling height
For Evidence Purposes:
Photos of
  Lights in place (before being removed)
  Close up of lamps/tubes showing wattage
  Close up of ballast showing details
  Recycling
Photos must be geotagged and time stamped
NB: For 240v Halogen lamps we also need photo of fitting

## Slide 12: Upgrade Lighting
Must appear on the ESS product search tool http://www.ess.nsw.gov.au/ELT/Product_Search
Close up photos of lamp and driver model numbers (geo-tagged photos taken BEFORE they are installed, as evidence they match ELT listing)

## Slide 13: Upgrade Lighting
Photos of:
  Lamp showing model number
  Driver showing model number (only non-integrated lamps)
  New lights in situ
LUX readings
We need a copy of invoice and customer payment receipt
Cost to OES must be >$5 per ESC

## Slide 14: Contractor Requirements
Sign Carbon Blue agreement
Inducted
Provide Certificates of Currency
Copies of licenses and certificates
For each project, provide:
  Safe Work Method Statement
  Installer declaration
  CCEW + attachment (doesn’t need to be sent to network operators, only needs to come to us)
  Signed copy of job specific Terms and Conditions

## Slide 15: Taking LUX Readings
Calibrated meter (need to know brand, model and serial number)
Must meet AS1680/BCA requirements PLUS 20% on average over measured area.
  LED upgrade lights are expected to last 10 years and are determined by regulator to depreciate by 20% over that time period, thus still meeting required AS1680/BCA requirements at end of life.
  Chart on next screen shows AS1680 minimum lux levels for specific class of tasks
LUX readings where possible should be taken at night and must not include natural daylight

## Slide 16
AS1680 Lux Level Requirements |  |  |  | 
Class of task |  | Recommended maintained Illuminance (lx) ESS Required Plus 20% | Characteristics of the activity/interior | Representative activities/interiors
Below Normal range of tasks and work places | Movement and Orientation | 40 50 | Interior rarely visited with visual tasks limited to movement and orientation | Corridors; cable tunnels; indoor storage tanks; walkways
 | Rough intermittent | 80 100 | Interiors requiring intermittent use with visual tasks limited to movement, orientation and course detail | Staff change rooms; live storage of bulky materials; dead storage of materials needing care; locker rooms; loading bays
Normal range of tasks and work places | Simple | 160 200 | Any continuously occupied interior where there are no tasks requiring perception of other than course detail. Occasional reading of clearly printed documents for short periods | Waiting rooms; staff canteens; rough checking stock; rough bench and machine work; entrance halls; general fabrication of structural steel’ casting concrete; automated process monitoring; turbine halls
 | Ordinary or moderately easy | 240 300 | Continuously occupied interiors with moderately easy visual tasks with high contrasts or large detail (<10 min arc) | School chalkboard and charts; medium woodworking; food preparation; counters for transactions.
 | Moderately difficult (Routine) | 320 400 | Areas where visual tasks are moderately difficult with moderate detail (5-10 min arc or tolerances to 125µm) or with low contrast | Routine office tasks, e.g. reading, writing, typing, enquiry desks
 | Moderately difficult (Medium) | 400 500 |  | Inspection of medium work; fine woodwork; car assembly
 | Difficult | 600 750 | Areas where visual tasks are difficult with small detail (3-5 min arc or tolerances to 25μm) or with low contrast | Drawing boards; most inspection tasks; proofreading; fine machine work; fine painting and finishing; colour matching
 | Very difficult | 800 1000 | Areas where visual tasks are very difficult with very small detail (2-3 min arc) or with very low contrast | Fine inspection; paint retouching; fine manufacture; grading of dark materials; colour matching of dyes
Above Normal range of tasks and work places | Extremely difficult | 1,200 1500 | Areas where visual tasks are extremely difficult with extremely small detail (1-2 min arc or tolerances below 25μm) or of low contrast. Visual aids may assist | Graphic arts inspection; hand tailoring; fine die sinking; inspection of dark goods; extra- fine bench work
 | Exceptionally difficult | 1,600 2000 | Areas where visual tasks are exceptionally difficult with exceptionally small detail (<1 min arc) or with very low contrasts. Visual aids will be of advantage | Finished fabric inspection; assembly of minute mechanisms, jewellery and watchmaking

## Slide 17: Select an appropriate test area within the space
Choose a representative sample of ‘class of tasks’ across the upgraded areas.
  For example, if the upgrade covers an office space, with multiple small offices that have the same lighting conditions, then a single test area in one office can be said to be representative of all the small offices. If there are also open plan office areas take additional lux readings in this area as well.
  For sites with multiple space types (e.g. office, warehouse, car park), you will need to take representative lux readings in each area.
Where the lighting layout follows a regular array, the test area should cover one representative selection of the array (e.g. over 4 or more lamp fittings)
For spaces with non-uniform lighting or different room conditions, select several measurement test areas
Natural light should be excluded from the test area as much as possible (i.e. away from windows or at night). Where this is not possible, two sets of measurements could be used, one with the lighting off, and the other with the lighting on, to determine the illuminance provided from the lighting

## Slide 18: Example of test area in a carpark
Test area size = 15m2 (3 x 5 meters)
Number of measurements = 15 (1m apart)
Number of luminaires covered by test area = 4
Height of measurements = 0.0m (floor)

## Slide 19: Example of test area in a small office
Test area size = 4.5m2
Number of measurements = 9 (0.5m apart)
Height of measurements = 0.8m (desk height)
Lux measurements must be taken at “working plane” level. So in office, this is desk height. For other areas like warehouse or car parks this is generally floor level.

## Slide 20: LUX level requirements
Take lux levels at night, or with daylight excluded from the space
  This can be achieved by taking two readings one with lights on and one with lights off. The difference would represent the light output of upgrade lighting.
Measurement points must be no more than 1m apart, and no closer than 1m to a wall
  For spaces greater than 25m2, the test area must be at least 9m2 and cover 4 luminaires. Make the test area larger if the luminaires are further apart.
  For spaces smaller than 25m2, the entire floor space should be measured, 1m away from walls with a minimum of 9 measurements. This means in small spaces, the measurements may be less than 1m apart.

## Slide 21: Record the measurements in a table
Area / room | Class of task | Size of test area (m2) | Number of measurements | Height of measurements from floor | Average Lux | Required Lux
Carpark 1 | Rough, intermittent use | 15m2 | 15 | 0.0 m | 112 lux | 100 Lux PASS
Office 1 | Moderately difficult | 4.5m2 | 9 | 0.9 m | 439 lux | 400 Lux PASS
Main office | Moderately difficult | 12m2 | 12 | 0.9 m | 758 | 400 Lux PASS

## Slide 22: Update ceiling plan with lux test areas
Upgrade Lighting Plan
must show where lux
readings were taken as
auditor will go to same
location to take their
own readings

## Slide 23: Recycling/Waste Management
Consider space requirements for temporary storage and discuss with site manager before installation.
Ensure your installation price includes waste management.
It is the contractors responsibility to remove metal and waste from lighting upgrade site.
  For evidence purposes, we require a certificate of destruction from metal recycler or tip indicating weight and description (e.g. light fittings & ballasts). Metal recyclers will not charge for disposal but most tips will.
All removed lamps/tubes must be sorted and packaged correctly so they are ready for collection by an authorised lamp recycler. Boxes must be labelled with lamp type and quantity. Tubes should not be taped but rather kept loose in boxes.
For large jobs take photo of all stacked lamp recycling cartons as this is often requested by lamp recycler.
Lamp counts must match what was removed/claimed in quotation and for ESC creation.